## Slide 1: Ground motion selection and scaling for NLRHA
Introduction to nonlinear response history analysis (NLRHA)
General workflow for NLRHA
Ground motion selection and scaling criteria
Example

## Slide 2: Motivation
Most extreme demands on structures vary with time!
Accurate simulation of the dynamic response of structures enables:
Safer designs
Cost-effective projects
Reliable performance
Functional/comfortable structures

## Slide 3: Static vs Dynamic analysis
Goal: quantify the response of a structure subjected to an external demand that varies with time.
P(t)
u
0.5Fs(t)
0.5Fs(t)
Fi(t)
Fd(t)
Fi(t) + Fd(t) + Fs(t) = P(t)
Equation of equilibrium:
P
u
0.5Fs
0.5Fs
Fs = P
Equation of equilibrium:
Dynamic
Static

## Slide 4: Terms of the dynamic equation of equilibrium
Fi(t) + Fd(t) + Fs(t) = P(t)
+ + = P(t)
Inertial force
Fi(t) =
Fictitious viscous damping force
Fd(t) =
Force of the structure
Fs(t) =
(ONLY for linear systems)
System properties:
m, , k, …
Period, T

## Slide 5: Ground motion time history analysis
Fi(t) + Fd(t) + Fs(t) = 0
u
0.5Fs(t)
Fi(t)
Fd(t)
ug
ug
0.5Fs(t)
+ + Fs(t) = 0
+ + Fs(t) = -
u
0.5Fs(t)
Fd(t)
0.5Fs(t)
Equivalent system:

## Slide 6: Effect of the vibration period
u
0.5Fs(t)
Fi(t)
Fd(t)
ug
ug
0.5Fs(t)
T = 2.0 s
T = 0.5 s
=0.05

## Slide 7: The concept of response spectrum
Displacement response spectrum
for this ground motion
(Garcia, 1998)
Period
Displacement response for systems with different period
Period
Displacement

## Slide 8: Pseudo-acceleration response spectrum
u
0.5Fs(t)
Fi(t)
Fd(t)
0.5Fs(t)
=pseudo-acceleration

## Slide 9: Linear vs Nonlinear
u
0.5Fs(t)
Fi(t)
Fd(t)
Fs(t) for NL systems
Displacement response
Force response
Plastic
Elastic

## Slide 10: Multiple degrees of freedom
(Zhong et al., 2020)
NIST Tall WSMFs (Galvis and Deierlein, 2022)

## Slide 11: Application of NLRHA in Engineering practice

## Slide 12: General workflow for NLRHA
Goal: quantify the response of a structure subjected to an external demand that varies with time.
Step 1: Build a numerical model of the structure
Step 2: Obtain the response spectrum target
Step 3: Select and scale ground motions
Step 4: Perform NLRHA
Step 5: Collect/parse results to interpret

## Slide 13: Step 1: Build a numerical model of the structure
Numerical model type:
Concentrated hinge model
Fiber hinge model
Distributed fiber element model
Continuous finite element model
Modeling assumptions:
2D Idealization vs. 3D model
Condensed vs. distributed mass
Gravity system and floor/slab constraints
Panel zone model
Software:
ETABS, PERFORM3D
ANASYS, ABAQUS
OpenSees
Fundamental period, T

## Slide 14: Step 2: Obtain the response spectrum target
Intensity measure:
PGA, PGV, PGD
Response spectrum (PSA or Sa)
Ground motion duration (e.g., DS5-75)
Single vs. vector intensity measure
Seismic hazard:
Magnitude, mechanism, slip, …
Distance, soil profiles/velocity model
Local soil properties
Seismic disaggregation (return period)
Target response spectrum:
Uniform hazard spectrum (UHS)
MCER
Conditional mean spectrum
Conditional spectrum
UHS
CMS
ASCE MCEr

## Slide 15: Step 2: Obtain the response spectrum target
MCER: Prescriptive intensity for new design
“It shall be permitted to use nonlinear response history analysis in accordance with the requirements of this chapter to demonstrate acceptable strength, stiffness, and ductility to resist maximum considered earthquake (MCER) shaking with acceptable performance…” - ASCE 7 Chapter 16
TL
Site coefficients
From Seismic maps
(ASCE/SEI 7, 2016)

## Slide 16: Step 2: Obtain the response spectrum target
(ASCE/SEI 7, 2016)

## Slide 17: Step 2: Obtain the response spectrum target

## Slide 18: Step 2: Obtain the response spectrum target
UHS: Uniform Hazard Spectrum
(Baker et al. 2022)
Seismic hazard curve:
Measure the likelihood of exceedance of a shaking intensity (e.g. Sa(T))
Uniform Hazard spectrum:
Collects the Sa(T) values with
a same exceedance rate at different periods.
Both are pre-computed for all the United States by the USGS

## Slide 19: Step 3: Select and scale ground motions
Key factors:
Number of records
Earthquake and site characteristics
Spectrum fitting (median/mean/std)
Period range
Scaling factor
Selection & scaling algorithm:
ASCE-7 type selection
CS-type selection
GCIM-type selection
Others:
Spectrally matching
Near-fault site
Seismic isolation

## Slide 20: Step 3: Select and scale ground motions
ASCE 7 16.1: “… Ground motion acceleration history histories shall be selected and modified in accordance with the procedures of Section 16.2…”
Eleven ground motions MINIMUM for each target spectrum
Ground motions shall have similar spectral shape to the target spectrum
Each ground motion shall be scaled such that the average of all ground motions is equal or greater that 90% of the target response spectrum for any period between 0.2 T1 ~ 1.5 T1
Ground motions shall be selected from events with generally same tectonic regime (e.g. strike-slip earthquakes).
Ground motions shall be selected from events with generally consistent magnitudes and fault distances as the target intensity level
For near-fault sites (“7-15km, 6-10km”)*, the proportion of selected ground motions with directivity effects
For 3D models, ground motions shall consist of pairs of orthogonal horizontal components.

## Slide 21: Step 3: Select and scale ground motions
Note: For 3D models one needs to select pairs of ground motions
Up
Down
(Garcia, 1998)
Error Index (EI) for spectrum fitting
A suite of M records, mth spectrum Sam
Periods considered [T1 , T2 , …, Tk ,…, TK]
A target spectrum: Satar

## Slide 22: Step 3: Select and scale ground motions
PEER Database
PEER offers ground motion recordings in the NGA West 2 database, which contains roughly 20000 ground motions from worldwide: https://ngawest2.berkeley.edu
Sign up (free) and log in to get access to the ground motion selection page
Demo live

## Slide 23: Step 4: Perform NLRHA
Algorithm:
Implicit: Newton, Newton Initial…
Explicit: central deferential
Damping:
Modal damping
Rayleigh damping (initial, committed, current)
Convergence:
Error indices
Time step
Number of iterations

## Slide 24: Step 5: Collect/parse results to interpret
Response check:
Peak story drift (structural damage)
Peak floor acceleration (non-structural damage)
Element forces (capacity design)
Statistics: Average, median, dispersion

## Slide 25: Example
Goal: quantify the response of a structure subjected to an external demand that varies with time.
Step 1: Build a numerical model of the structure
Step 2: Obtain the response spectrum target
Step 3: Select and scale ground motions
Step 4: Perform NLRHA
Step 5: Collect/parse results to interpret

## Slide 26: Example
Demo live

## Slide 27: Example

## Slide 28: Example

## Slide 29: Example

## Slide 30: Example

## Slide 31: Example

## Slide 32: Example

## Slide 33: Ground motion selection and scaling for NLRHA
Introduction to nonlinear response history analysis (NLRHA)
General workflow for NLRHA
Ground motion selection and scaling criteria
Example